## Slide 1: Your Smart Automatic Humidifier
Andrew Sherwin - Woojin Kim - Jalen Chen
TA: Surya Vasanth
Professor: Dr. Jonathon Schuh
Notes: Every

## Slide 2: Agenda
Problem & Solution
Visual Aid
High Level Requirements
Block Diagram
Webserver and Algorithm
RV Table
Project Achievements
Future Plans
Notes: Andrew

## Slide 3: Problem
Environmental Protection Agency highly suggests 30-50% humidity indoors
Chemicals, gasses, pollen, mold, and other particles are reduced
Most cheap humidifiers are bad for the user's health
  Warm mist – cause nasal passages to swell
  Ultrasonic – displaces minerals and bacteria
Manual humidifiers can over/under humidity
Humidifiers on market need manual water refilling
Notes: Andrew

## Slide 4: Solution
Cool mist humidifier
  Good for health
  Evaporates water off filter
Automatic on/off humidifier based on humidity
Remote humidity sensing via 3 sensors
Automatic water refill via water valve with water level sensing
Notes: Andrew

## Slide 5: Visual Aid
Notes: Andrew

## Slide 6: Visual Aid - Component
Notes: Andrew
Two sensors locations
Water valve and Fan
-> all talks to ESP32

## Slide 7: High Level 1
Humidifier's ESP32 communication with three different sensors via 2.4GHz Wi-Fi
Average humidity data from three sensors
Create temperature dependent humidity calculation algorithm
Notes: Jalen
Talk about why we chose 2.4GHz wifi over bluetooth (range and wall penetration)

## Slide 8: High Level 2
Open/close valve to refill the water tank
Two water level sensors GPIO input to ESP32
Max capacity of the water tank: 4.16 liters
Filter absorbs around 150 milliliters ± 5 milliliters
Evaporation rate approximately 173 milliliters per hour (in 40% humidity room)
Notes: Jalen
173 milliliter is from (max capacity)/(time for tank to empty) = 4160/24-hour = 173.33 milliliter
Filter absorbing 150 milliliter is from wringing out filter and measuring the volume

## Slide 9: High Level 3
On/off fan based on pre-configured ideal humidity range, 35% and 50% humidity, based on an algorithm averaging the readings from 3 sensors
Actuate relay with LED output for ON signal
Theoretical estimation of 44ns response time to on/off the humidifier’s fan (w/o runtime)
High voltage (120V AC) components does not interfere with low voltage components (< 12V DC)
Notes: Woojin
44ns from: SHT45 -> ESP32 -> wifi of 6m range -> ESP32 -> algorithm -> relay actuation
  1 bit of data only
Realistically:
  2 bytes of data for humidity, 2 bytes of data for temperature
  Data needs to be unpacked by ESP32 (sensor subsystem) and repacked for WiFi transmission -> ESP32 (humidifier) needs to unpack data -> send acknoledgement back -> ESP32 (sensor) unpacks data -> output on console
  That is why we got 45,000ns

## Slide 10: Block Diagram
Notes: andrew

## Slide 11: Block Diagram - Humidifier
Notes: andrew

## Slide 12: Current vs Original Humidifier Subsystem
Original Block Diagram – Project Proposal

## Slide 13: Humidifier Subsystem PCBs
Humidifier PCB Rev0
Humidifier PCB Rev4

## Slide 14: Block Diagram - Sensor
Notes: Andrew

## Slide 15: Sensor Subsystem PCBs
Humidifier PCB Rev0

## Slide 16: Web Server & Algorithm
WiFi access with mDNS
Auto/Manual Mode
(Fan/Valve off when Auto->Manual)
Signal Loss Detection
Refreshes every 2s
Warmer air can handle more moisture
-> new Humidity target based on average temperature
(if avg. Temp < 20'C -> 35~42.5% Rh)
(if avg. Temp > 22'C -> 42.5~50% Rh)
(else, 35~50% Rh)
Notes: Woojin

## Slide 17: RV Table – Central Humidifier Subsystem (1)
3.3V linear regulator output
Temperature reading with laser
5V linear regulator output
Notes: jalen

## Slide 18: RV Table – Central Humidifier Subsystem (1)
Chart: 3.3V vs Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Voltage | 3.3012 | 3.3016 | 3.3016 | 3.3015 | 3.3015 | 3.3014 | 3.3015 | 3.3014 | 3.3016 | 3.3016 | 3.3015 | 3.3014 | 3.3014 | 3.3015 | 3.3016 | 3.3016 | 3.3014 | 3.3016 | 3.3015 | 3.3014 | 3.3016 | 3.3015 | 3.3015 | 3.3016 | 3.3014 | 3.3015 | 3.3014 | 3.3015 | 3.3016 | 3.3014 | 3.3014 | 3.3014 | 3.3012 | 3.3013 | 3.3014 | 3.3013 | 3.3016 | 3.3016 | 3.3015 | 3.3014 | 3.3014 | 3.3015 | 3.3015 | 3.3016 | 3.3014 | 3.3015 | 3.3014 | 3.3015 | 3.3016 | 3.3016 | 3.3015 | 3.3014 | 3.3015 | 3.3014 | 3.3015 | 3.3015 | 3.3015 | 3.3016 | 3.3016 | 3.3014
Chart: 5V vs Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Voltage | 5.0012 | 5.0012 | 5.001 | 5.0008 | 5.0011 | 5.0008 | 5.0009 | 5.0012 | 5.0013 | 5.0009 | 5.0008 | 5.0013 | 5.0011 | 5.0013 | 5.0008 | 5.0009 | 5.0012 | 5.0013 | 5.0012 | 5.0008 | 5.0011 | 5.001 | 5.001 | 5.0008 | 5.0012 | 5.0013 | 5.0011 | 5.0011 | 5.0009 | 5.0013 | 5.0013 | 5.0011 | 5.001 | 5.0011 | 5.0012 | 5.0009 | 5.001 | 5.0012 | 5.001 | 5.0008 | 5.0013 | 5.0011 | 5.0013 | 5.0013 | 5.0011 | 5.0013 | 5.0008 | 5.0012 | 5.001 | 5.0014 | 5.0014 | 5.0013 | 5.001 | 5.0008 | 5.0008 | 5.0009 | 5.001 | 5.0012 | 5.0011 | 5.0013
Notes: jalen

## Slide 19
RV Table – Central Humidifier Subsystem (1)

## Slide 20: RV Table – Central Humidifier Subsystem (2)
LED light control example
Temperature reading example
Notes: Jalen maybe andrew

## Slide 21: RV Table – Central Humidifier Subsystem (3)
LED light when valve is on
12V output to water valve
Notes: Jalen, maybe andrew

## Slide 22: RV Table – Central Humidifier Subsystem (4)
Water level sensor contact water
Water-valve off when water detected
Notes: jalen

## Slide 23: RV Table – Humidity Sensor Subsystem (1)
3.3V linear regulator output
Temperature reading with laser
5V linear regulator output
Notes: woojin

## Slide 24: RV Table – Humidity Sensor Subsystem (1)
Chart: 5V Input VS Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Voltage | 4.999 | 4.9998 | 4.9999 | 4.9998 | 5.0003 | 5.0001 | 4.9999 | 4.9998 | 4.9999 | 5.0002 | 5.0002 | 5.0002 | 5.0001 | 5.0002 | 4.9999 | 5.0003 | 4.9999 | 5.0001 | 5.0001 | 4.9998 | 5 | 5 | 5.0003 | 5.0002 | 5.0002 | 5.0002 | 5.0001 | 5 | 5.0003 | 5 | 4.9998 | 5.0001 | 5.0002 | 4.9999 | 4.9998 | 5.0003 | 5 | 4.9998 | 5 | 5.0004 | 5.0003 | 4.9999 | 5.0001 | 5.0003 | 5 | 4.9999 | 4.9998 | 5 | 5.0002 | 5.0001 | 4.9998 | 5.0003 | 5.0001 | 5.0002 | 5.0003 | 4.9999 | 5.0001 | 5.0003 | 5 | 5.0003
Chart: 3.3V vs Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Voltage | 3.3005 | 3.3004 | 3.3002 | 3.3005 | 3.3005 | 3.3003 | 3.3002 | 3.3005 | 3.3 | 3.3 | 3.3 | 3.3001 | 3.3003 | 3.3 | 3.3 | 3.3004 | 3.3004 | 3.3003 | 3.3004 | 3.3 | 3.3002 | 3.3005 | 3.3005 | 3.3 | 3.3004 | 3.3 | 3.3004 | 3.3001 | 3.3004 | 3.3 | 3.3 | 3.3004 | 3.3004 | 3.3001 | 3.3001 | 3.3 | 3.3002 | 3.3004 | 3.3004 | 3.3005 | 3.3005 | 3.3002 | 3.3003 | 3.3004 | 3.3005 | 3.3004 | 3.3003 | 3.3005 | 3.3003 | 3.3005 | 3.3 | 3.3 | 3.3001 | 3.3 | 3.3 | 3.3003 | 3.3 | 3.3004 | 3.3001 | 3.3001
Notes: woojin

## Slide 25: RV Table – Humidity Sensor Subsystem (1)

## Slide 26: RV Table – Humidity Sensor Subsystem (2)
Commercial humidity and temperature sensor verification
Notes: woojin

## Slide 27: Project Achievements and Successes
Sensor Subsystem reads temperature and humidity data from SHT45
Sensor Subsystem communicates with Humidifier Subsystem with Wi-Fi
Humidifier Subsystem successfully activates humidifier
Humidifier Subsystem successfully activates water valve
Humidifier Subsystem successfully reads from water level sensors
Bonus:
  User Interface through access point to control Humidifier Subsystem
  Reliability tested for 4 weeks, running 24/7
Notes: Andrew

## Slide 28: Challenges
No failures on current design
Hardware
  Initial 12V input to PCB was too high for Linear Voltage Regulator
  Relay design
    Isolation, creepage, clearance
  Optocoupler
  SHT45 location and isolation
  Modular overall design
Software
  Concurrent multi-node communication
Notes: Andrew

## Slide 29: Conclusion and Future Plans
Integrate with Amazon Alexa, Apple HomeKit, and Google Assistant
Change linear voltage regulator to buck converter
Further compact PCB
  Remove ESP32 programming components
Create original AC/DC Converter if budget allows
Improve PCB enclosure design
Improve UI design
Potentially remove water level sensor and water valve
  Making product modular for all manual humidifiers
"Students learn the most then they struggle with challenges" - Minh Do
Notes: Andrew

## Slide 30: Your Oasis Awaits: Refresh, Rejuvenate, Breathe
Notes: Everyone//end