## Slide 1: Your Smart Automatic Humidifier
Andrew Sherwin - Woojin Kim - Jalen Chen
TA: Surya Vasanth
Professor: Dr. Jonathon Schuh
Notes: Every

## Slide 2: Agenda
Problem & Solution
Visual Aid
High Level Requirements
Block Diagram
RV Table
Project Achievements
Future Plans
Notes: Andrew

## Slide 3: Problem
Environmental Protection Agency highly suggests 30-50% humidity indoors
Chemicals, gasses, pollen, mold, and other particles are reduced
Most cheap humidifiers are bad for the user's health
  Warm mist – cause nasal passages to swell
  Ultrasonic – displaces minerals and bacteria
Manual humidifiers can over/under humidity
Humidifiers on market need manual water refilling
Notes: Andrew

## Slide 4: Solution
Cool mist humidifier
  Good for health
  Evaporates water off filter
Remote humidity sensing via 3 sensors
Automatic on/off humidifier based on humidity
Automatic water valve with water level sensing
Notes: Andrew

## Slide 5: Visual Aid
Notes: Woojin
Talking through 2.4 GHz

## Slide 6: Visual Aid - Component
Notes: Woojin
Two sensors locations
Water valve and Fan
-> all talks to ESP32

## Slide 7: High Level 1
Humidifier's ESP32 communication with three different sensors via 2.4GHz Wi-Fi
Average humidity data from three sensors
Create temperature dependent humidity calculation algorithm
Notes: Jalen

## Slide 8: High Level 2
Open/close valve to refill the water tank
Two water level sensors GPIO input to ESP32
Max capacity of the water tank: 4.16 liters
Filter absorbs around 150 milliliters ± 5 milliliters
Evaporation rate approximately 173 milliliters per hour (in 40% humidity room)
Notes: Jalen
173 milliliter is from (max capacity)/(time for tank to empty) = 4160/24-hour = 173.33 milliliter
Filter absorbing 150 milliliter is from wringing out filter and measuring the volume

## Slide 9: High Level 3
On/off fan based on pre-configured ideal humidity range, 35% and 50% humidity, based on an algorithm averaging the readings from 3 sensors
Actuate relay with LED output for ON signal
Theoretical estimation of 44ns response time to on/off the humidifier’s fan (w/o runtime)
High voltage (120V AC) components does not interfere with low voltage components (< 12V DC)
Notes: Woojin
44ns from: SHT45 -> ESP32 -> wifi of 6m range -> ESP32 -> algorithm -> relay actuation

## Slide 10: Block Diagram
Notes: andrew

## Slide 11: Block Diagram - Humidifier
Notes: andrew

## Slide 12: Block Diagram - Sensor
Notes: Andrew

## Slide 13: Demonstration

## Slide 14: RV Table – Central Humidifier Subsystem (1)
3.3V linear regulator output
Temperature reading with laser
5V linear regulator output
Notes: jalen

## Slide 15: RV Table – Central Humidifier Subsystem (1)
Chart: 3.3V vs Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Voltage | 3.3012 | 3.3016 | 3.3016 | 3.3015 | 3.3015 | 3.3014 | 3.3015 | 3.3014 | 3.3016 | 3.3016 | 3.3015 | 3.3014 | 3.3014 | 3.3015 | 3.3016 | 3.3016 | 3.3014 | 3.3016 | 3.3015 | 3.3014 | 3.3016 | 3.3015 | 3.3015 | 3.3016 | 3.3014 | 3.3015 | 3.3014 | 3.3015 | 3.3016 | 3.3014 | 3.3014 | 3.3014 | 3.3012 | 3.3013 | 3.3014 | 3.3013 | 3.3016 | 3.3016 | 3.3015 | 3.3014 | 3.3014 | 3.3015 | 3.3015 | 3.3016 | 3.3014 | 3.3015 | 3.3014 | 3.3015 | 3.3016 | 3.3016 | 3.3015 | 3.3014 | 3.3015 | 3.3014 | 3.3015 | 3.3015 | 3.3015 | 3.3016 | 3.3016 | 3.3014
Chart: 5V vs Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Voltage | 5.0012 | 5.0012 | 5.001 | 5.0008 | 5.0011 | 5.0008 | 5.0009 | 5.0012 | 5.0013 | 5.0009 | 5.0008 | 5.0013 | 5.0011 | 5.0013 | 5.0008 | 5.0009 | 5.0012 | 5.0013 | 5.0012 | 5.0008 | 5.0011 | 5.001 | 5.001 | 5.0008 | 5.0012 | 5.0013 | 5.0011 | 5.0011 | 5.0009 | 5.0013 | 5.0013 | 5.0011 | 5.001 | 5.0011 | 5.0012 | 5.0009 | 5.001 | 5.0012 | 5.001 | 5.0008 | 5.0013 | 5.0011 | 5.0013 | 5.0013 | 5.0011 | 5.0013 | 5.0008 | 5.0012 | 5.001 | 5.0014 | 5.0014 | 5.0013 | 5.001 | 5.0008 | 5.0008 | 5.0009 | 5.001 | 5.0012 | 5.0011 | 5.0013
Notes: jalen

## Slide 16: RV Table – Central Humidifier Subsystem (2)
LED light control example
Temperature reading example
Notes: jalen

## Slide 17: RV Table – Central Humidifier Subsystem (3)
LED light when valve is on
12V output to water valve
Notes: jalen

## Slide 18: RV Table – Central Humidifier Subsystem (4)
Water level sensor contact water
Water-valve off when water detected
Notes: jalen

## Slide 19: RV Table – Humidity Sensor Subsystem (1)
3.3V linear regulator output
Temperature reading with laser
5V linear regulator output
Notes: woojin

## Slide 20: RV Table – Humidity Sensor Subsystem (1)
Chart: 5V Input VS Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Voltage | 4.999 | 4.9998 | 4.9999 | 4.9998 | 5.0003 | 5.0001 | 4.9999 | 4.9998 | 4.9999 | 5.0002 | 5.0002 | 5.0002 | 5.0001 | 5.0002 | 4.9999 | 5.0003 | 4.9999 | 5.0001 | 5.0001 | 4.9998 | 5 | 5 | 5.0003 | 5.0002 | 5.0002 | 5.0002 | 5.0001 | 5 | 5.0003 | 5 | 4.9998 | 5.0001 | 5.0002 | 4.9999 | 4.9998 | 5.0003 | 5 | 4.9998 | 5 | 5.0004 | 5.0003 | 4.9999 | 5.0001 | 5.0003 | 5 | 4.9999 | 4.9998 | 5 | 5.0002 | 5.0001 | 4.9998 | 5.0003 | 5.0001 | 5.0002 | 5.0003 | 4.9999 | 5.0001 | 5.0003 | 5 | 5.0003
Chart: 3.3V vs Time
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
Voltage | 3.3005 | 3.3004 | 3.3002 | 3.3005 | 3.3005 | 3.3003 | 3.3002 | 3.3005 | 3.3 | 3.3 | 3.3 | 3.3001 | 3.3003 | 3.3 | 3.3 | 3.3004 | 3.3004 | 3.3003 | 3.3004 | 3.3 | 3.3002 | 3.3005 | 3.3005 | 3.3 | 3.3004 | 3.3 | 3.3004 | 3.3001 | 3.3004 | 3.3 | 3.3 | 3.3004 | 3.3004 | 3.3001 | 3.3001 | 3.3 | 3.3002 | 3.3004 | 3.3004 | 3.3005 | 3.3005 | 3.3002 | 3.3003 | 3.3004 | 3.3005 | 3.3004 | 3.3003 | 3.3005 | 3.3003 | 3.3005 | 3.3 | 3.3 | 3.3001 | 3.3 | 3.3 | 3.3003 | 3.3 | 3.3004 | 3.3001 | 3.3001
Notes: woojin

## Slide 21: RV Table – Humidity Sensor Subsystem (2)
Commercial humidity and temperature sensor verification
Notes: woojin

## Slide 22: Project Achievements
Sensor Subsystem reads temperature and humidity data from SHT45
Sensor Subsystem communicates with Humidifier Subsystem with Wi-Fi
Humidifier Subsystem successfully activates humidifier
Humidifier Subsystem successfully activates water valve
Humidifier Subsystem successfully reads from water level sensors
Bonus:
  User Interface through access point to control Humidifier Subsystem
Notes: Andrew

## Slide 23: Future Plans
Integrate with Amazon Alexa, Apple HomeKit, and Google Assistant
Further compact PCB
  Remove ESP32 programming components
Improve PCB enclosure design
Improve UI design
Potentially remove water level sensor and water valve
Consult with business consultants to push product on market
Notes: Andrew

## Slide 24: Your Oasis Awaits: Refresh, Rejuvenate, Breathe
Notes: Everyone//end